## Slide 1: CONCEPTUAL DESIGN PRESENTATION Devices Trying to Score in Each Others’ Goals 27.12.2018
PITECH

## Slide 2: CEO FATMA NUR ARABACI
PITECH

## Slide 3: Presentation Outline
PITECH
01
04
02
03
05
Company Profile
Problem Statement
Objectives
Solution Approaches
Plans
06
Conclusion

## Slide 4: COMPANY PROFILE Shareholders
PITECH
CEO Fatma Nur ARABACI 2030047 | CMO Berkay GÖKSU 2030757 | CTO Furkan Bahadır ELİK 2030518 | CFO Aycan BEYENİR 2030328 | COO İrem COŞKUN 2030419

## Slide 5
Mission
To provide creative and reliable solutions that fulfill the needs of industry in the field of Industrial robot applications.
Vision
To become the most compelling technology company by driving the industry’s transition to smart manufacturing.
PITECH
COMPANY PROFILE Mission & Vision

## Slide 6: PROBLEM STATEMENT
PITECH
Try to score in the opponents’ goal
Try to defend our own goal
Control via tele-operator (non-autonomous)
~75 cm

## Slide 7
PITECH
Our Robot
Robot Side
Controller Side
>= 30 m
Opponents’ Robot
Half Field Line
Oppenents’ Goal
Our Goal
The ball

## Slide 8: PROBLEM STATEMENT Requirements & Constraints
PITECH
Half Field Line
Oppenents’ Goal
Our Goal
Goal line should be two times of our robots’ diameter
20 sec restriction
Robot should stay in its’ half field
Carrying, grasping and scooping the ball is not allowed.
Within $200 budget

## Slide 9: OBJECTIVES Performance Related Objectives
PITECH
Range
Power Consumption
Transmission Delay
Perfect–> 30 min of operation
Sufficient -> 15 min of operation
Poor -> 5 min of operation
Perfect–> 100 ms delay
Good -> 400 ms delay
Sufficient-> 600 ms delay
Poor-> 1 sec delay
Perfect–>more than 30m indoor
Sufficient-> 30 m indoor
Poor/Failure-> less than 30 m indoor

## Slide 10: CMO BERKAY GÖKSU
PITECH

## Slide 11: Overall Block Diagram Flow Chart Shooting Subsystem Motion Subsystem
PITECH

## Slide 12: Block Diagram of Robot Side
PITECH

## Slide 13: Block Diagram of Controller Side
PITECH

## Slide 14: Flow Chart
PITECH

## Slide 15: SUBSYSTEMS
Shooting Subsystem
Motion Subsystem
Communication Subsystem
Power Supply Subsystem
Main Processor Subsystem
PITECH

## Slide 16: Shooting Subsystem
PITECH

## Slide 17
PITECH
Spring actuated
Very powerful, much energy can be stored
Simple mechanism (wound up, held, and released)

## Slide 18: Motion Subsystem
PITECH
2 DC Motors and encoders & 2 Drive Wheels
2 Caster Wheels

## Slide 19: Differential Drive
PITECH
Easy to program
Well controlled
Simple
Low Cost

## Slide 20: CTO FURKAN BAHADIR ELİK
PITECH

## Slide 21: Communication Subsystem Command Transmission
PITECH

## Slide 22: Communication Subsystem Command Transmission
FM Radio infrastructure
Frequency shift keying with FM carrier
PITECH

## Slide 23: Controller Side
PITECH

## Slide 24: Controller Side
PITECH
Button Press

## Slide 25: Controller Side
PITECH
Button Press
A command is generated

## Slide 26: Controller Side
PITECH
Button Press
A command is generated
Raspberry Pi

## Slide 27: Controller Side
PITECH
Button Press
A command is generated
Raspberry Pi
The command is received

## Slide 28: Controller Side
PITECH
Button Press
A command is generated
Raspberry Pi
The command is received
Program

## Slide 29: Controller Side
PITECH
Button Press
A command is generated
Raspberry Pi
The command is received
Program
Received command is interpreted and a sine wave is generated

## Slide 30: Controller Side
PITECH
Button Press
A command is generated
Raspberry Pi
The command is received
Program
Received command is interpreted and a sine wave is generated
50 Hz < fn < 20 kHz
1st command
2nd command
3rd command
4th command
5th command
f1
f2
f3
f4
f5
FSK

## Slide 31: Controller Side
PITECH
Button Press
A command is generated
Raspberry Pi
The command is received
Program
Received command is interpreted and a sine wave is generated
Program
Generated sine wave is FM modulated with pre-chosen fc

## Slide 32: Controller Side
PITECH
Button Press
A command is generated
Raspberry Pi
The command is received
Program
Received command is interpreted and a sine wave is generated
Program
Generated sine wave is FM modulated with pre-chosen fc
87.5 MHz < fc < 108 MHz

## Slide 33: Controller Side
PITECH
Button Press
A command is generated
Raspberry Pi
The command is received
Program
Received command is interpreted and a sine wave is generated
Program
Generated sine wave is FM modulated with pre-chosen fc
Raspberry Pi
Generated FM modulated signal is fed to an external antenna

## Slide 34: Controller Side
PITECH
Button Press
A command is generated
Raspberry Pi
The command is received
Program
Received command is interpreted and a sine wave is generated
Program
Generated sine wave is FM modulated with pre-chosen fc
Raspberry Pi
Generated FM modulated signal is fed to an external antenna
Antenna
Generated FM wave is transmitter to air

## Slide 35: Robot Side
PITECH

## Slide 36: Robot Side
PITECH
Antenna

## Slide 37: Robot Side
PITECH
Antenna
Transmitted FM wave received

## Slide 38: Robot Side
PITECH
Antenna
Transmitted FM wave received
FM Radio

## Slide 39: Robot Side
PITECH
Antenna
Transmitted FM wave received
FM Radio
Received FM wave demodulated and gain controlled
Provides FM demodulation and automatic gain control (AGC)

## Slide 40: Robot Side
PITECH
Antenna
Transmitted FM wave received
FM Radio
Received FM wave demodulated and gain controlled
Arduino

## Slide 41: Robot Side
PITECH
Antenna
Transmitted FM wave received
FM Radio
Received FM wave demodulated and gain controlled
Arduino
Demodulated FSK signal received

## Slide 42: Robot Side
PITECH
Antenna
Transmitted FM wave received
FM Radio
Received FM wave demodulated and gain controlled
Arduino
Demodulated FSK signal received
Program

## Slide 43: Robot Side
PITECH
Antenna
Transmitted FM wave received
FM Radio
Received FM wave demodulated and gain controlled
Arduino
Demodulated FSK signal received
Program
FSK signal interpreted and its frequency is obtained
Frequency = 1/Period

## Slide 44: Robot Side
PITECH
Antenna
Transmitted FM wave received
FM Radio
Received FM wave demodulated and gain controlled
Arduino
Demodulated FSK signal received
Program
FSK signal interpreted and its frequency is obtained
Program

## Slide 45: Robot Side
PITECH
Antenna
Transmitted FM wave received
FM Radio
Received FM wave demodulated and gain controlled
Arduino
Demodulated FSK signal received
Program
FSK signal interpreted and its frequency is obtained
Program
The command is received based on received frequency
1st command
2nd command
3rd command
4th command
5th command
f1
f2
f3
f4
f5

## Slide 46: Robot Side
PITECH
Antenna
Transmitted FM wave received
FM Radio
Received FM wave demodulated and gain controlled
Arduino
Demodulated FSK signal received
Program
FSK signal interpreted and its frequency is obtained
Program
The command is received based on received frequency
Program

## Slide 47: Robot Side
PITECH
Antenna
Transmitted FM wave received
FM Radio
Received FM wave demodulated and gain controlled
Arduino
Demodulated FSK signal received
Program
FSK signal interpreted and its frequency is obtained
Program
The command is received based on received frequency
Program
The command is executed
GO AHEAD!

## Slide 48: CFO AYCAN BEYENİR
PITECH

## Slide 49
PITECH
Visual Information Transmission Part of Communication Subsystem
Power Supply Subsystem

## Slide 50
PITECH
Communication Subsystem: Visual Information Transmission
The system must;
Transfer all necessary information,
Introduce minimum transmission delay,
Provide stable flow of information,
Inexpensive.

## Slide 51
PITECH
Main Plan
AKK KC03 FPV Camera with 600MW Transmitter (n.d.). Retrieved from https://www.akktek.com/akk-kc03.html
FPV Camera with 600mW transmitter
This module provide;
High quality video acquisition and transmission
Approximately zero delay
Stable video stream over 30+ meter
Low cost

## Slide 52
PITECH
Backup Plan
Current capture of Camera
Image Processing
Information 1
Information 2
Information 3
Visual
Information Transmitter
Visual
Information Receiver
Visual Rebuilt
Screen
Robot
Telecontroller

## Slide 53
PITECH
Power Subsystem
For best performance this subsystem must:
Provide isolation between subsystems,
Provide 5V and 12V supply,
Lightweight,
Inexpensive.

## Slide 54
PITECH
Li-Po Battery (n.d) Retrieved from www.motionrc.com/products/admiral-3300mah
Lithium-Polymer & Lithium Ion
Li-Ion Powerbank (n.d) Retrieved from www.snapdeal.com/product/asus-blue-zen-power-bank
Main Plan

## Slide 55
PITECH
Backup Plan
Isolation Methods:
Capacitor connection to motor terminals
Choke Ferrite
Short twisted motor cables
High Pass filter for supply
Diode connections
Choke Ferrite (n.d.) retrieved from
picclick.com/5pcs-7mm-Noise-Suppressor
VDD
supply
VDD motor
Gnd
High Pass filter

## Slide 56: COO İREM COŞKUN
PITECH

## Slide 57
Cost Analysis
Time Plan
Deliverables
Conclusion
PITECH

## Slide 58: Cost Analysis
PITECH
Materials | Number | Price per each | Total Price
Clone Arduino Uno | 1 | $5 | $5
Raspberry Pi 3 | 1 | $40 | $40
DC Motors | 2 +1 | $10 / $5 | $25
Gearbox | 3 | $5 | $15
Cables & Connectors | nAn | $6 | $6
Battery | 2 | $15 | $30
Dummy Robot | 1 | $2 | $2
Balls | 2 | $0.25 | $0.5
Chassis | 1 | $10 | $10
Encoders | 2 | $5 | $10
Play Field Walls | 3 | $1 | $3
3D Printed Parts | nAn | $8 | $8
FPV Drone Kit | 1 | $35 | $35
Wheels (Standard + Ball) | 2 + 2 | $2 / $1 | $6
Sum : $195.5 |  |  | 

## Slide 59: Time Plan
PITECH
Sep ‘18
Oct ‘18
Nov ‘18
Dec ‘18
Today
Company Foundation
Business Statement
Project Evaluation
Research
Brainstorming
Initial solution approaches
Tests
Demonstration phase I
Conceptual design

## Slide 60: Future Plans
PITECH
Jan ‘19
Feb ‘19
Mar ‘19
Apr ‘19
DEMO
DAY
Motion subsystem implementation
Shooting subsystem implementation
Testing Equipment
Testing individual subsystems
Testing overall system
May ‘19
Implementation of Overall System
Final Tests

## Slide 61: Deliverables
PITECH
Gallery For > Box Wallpapers. (2018). Retrieved from http://feelgrafix.com/data_images/out/28/984471-box.jpg

## Slide 62: Deliverables
PITECH
Main Unit
01

## Slide 63: Deliverables
PITECH
Main Unit
Communication Module
01
02
remote control antenna drone technology wireless. (2018). Retrieved from
https://www.shutterstock.com/image-vector/remote-control-antenna-drone-technology-wireless-759977725

## Slide 64: Deliverables
PITECH
Main Unit
Communication Module
Batteries
01
02
03
E-flite3000mAh 3S 11.1V 30C LiPo Battery for RC Aircraft. (2018). Retrieved from https://www.bhphotovideo.com/c/product/1127413-REG/e_flite_eflb30003s30_3000mah_3s_11_1v_30c.html
remote control antenna drone technology wireless. (2018). Retrieved from
https://www.shutterstock.com/image-vector/remote-control-antenna-drone-technology-wireless-759977725

## Slide 65
PITECH
Game Field & A Ball
04
Deliverables
Projects – Capstone Design. (2018). Retrieved
from http://capstone.eee.metu.edu.tr/projects/

## Slide 66
PITECH
Game Field & A Ball
A Dummy Robot
04
05
Deliverables
Projects – Capstone Design. (2018). Retrieved
from http://capstone.eee.metu.edu.tr/projects/

## Slide 67
PITECH
Game Field & A Ball
A Dummy Robot
User Guide & Warranty Certificate
04
05
06
Deliverables
Projects – Capstone Design. (2018). Retrieved
from http://capstone.eee.metu.edu.tr/projects/
Phone | Blue Ridge. (2018). Retrieved from http://www.brctv.com/phone

## Slide 68: Conclusion
PITECH

## Slide 69: Conclusion
PITECH
Company Profile

## Slide 70: Conclusion
PITECH
Company Profile
Problem Statement

## Slide 71: Conclusion
PITECH
Company Profile
Problem Statement
Objectives

## Slide 72: Conclusion
PITECH
Company Profile
Problem Statement
Objectives
Solution Aproaches on Subsystems

## Slide 73: Conclusion
PITECH
Company Profile
Problem Statement
Objectives
Solution Aproaches on Subsystems
Proof of Concept

## Slide 74: Conclusion
PITECH
Company Profile
Problem Statement
Objectives
Solution Aproaches on Subsystems
Proof of Concept
Plans

## Slide 75: References
Gallery For > Box Wallpapers. (2018). Retrieved from http://feelgrafix.com/data_images/out/28/984471-box.jpg
E-flite3000mAh 3S 11.1V 30C LiPo Battery for RC Aircraft. (2018). Retrieved from https://www.bhphotovideo.com/c/product/1127413-REG/e_flite_eflb30003s30_3000mah_3s_11_1v_30c.html
remote control antenna drone technology wireless. (2018). Retrieved from https://www.shutterstock.com/image-vector/remote-control-antenna-drone-technology-wireless-759977725
Projects – Capstone Design. (2018). Retrieved from http://capstone.eee.metu.edu.tr/projects/
Phone | Blue Ridge. (2018). Retrieved from http://www.brctv.com/phone
AKK KC03 FPV Camera with 600MW Transmitter (n.d.). Retrieved from https://www.akktek.com/akk-kc03.html
Li-Po Battery (n.d) Retrieved from www.motionrc.com/products/admiral-3300mah
Li-Ion Powerbank (n.d) Retrieved from www.snapdeal.com/product/asus-blue-zen-power-bank
PITECH

## Slide 76
PITECH

## Slide 77: Contact Us
PITECH
potatointegrated@gmail.com
1427.Cadde İşçi Blokları Mah. 10. Yıldız Blok No: 35/23 A
Çankaya/Ankara
facebook.com/PITECH
linkedin.com/potatointegrated