## Slide 1
Potato: A tele-operated robot trying to
shoot and score in opponent’s goal
PITECH (Potato Integrated Technologies) was founded in 2018 with five shareholders from different backgrounds. As PITECH engineers our aim is to build a robot that we can control from a distance up to at least 30 meter indoor with a remote controller. This robot tries to score within a playfield in its opponent’s goal and defend its own goal without actually monitoring the play-field with naked eye.
Fatma Nur Arabacı - CEO
Furkan Bahadır ELİK - CTO
İrem COŞKUN - COO
Berkay GÖKSU - CMO
Aycan BEYENİR - CFO
SHAREHOLDERS
DELIVERABLES
Potato Robot Controller Unit 2 Li-Po Battery 3 Game Field Walls 2 Balls A Dummy Robot User Manual 2-year Warranty Software Pack
Special Thanks to our Supervisor Arzu Tuncay KOÇ
User friendly control module
Fast-learning curve for the user
Wide field of view
OUTSTANDING FEATURES
Materials |  | Cost
DC Motor with Gearbox |  | 2 x $15
L298N Motor Driver |  | 2 x $1.5
Push-Pull Solenoid |  | 1 x $4
Clone Arduino Uno |  | 1 x $4
Clone Arduino Mega |  | 1 x $10
FPV Drone Kit |  | 1 x $35
NRF24L01+PA+LNA SMA |  | 2 x $4
Joystick |  | 1 x $0.50
LCD screen |  | 1 x $30
900 mAh Li-Po Battery |  | 1 x $14
1350 mAh Li-Po Battery |  | 1 x $18
Buck-Boost Converter |  | 3 x $1
Plexiglass Chassis |  | 1 x $6
Standard Wheels |  | 2 x $2
Ball Wheel |  | 3 x $1
Cables & Connectors |  | $6
Structural connections |  | $3
Dummy Robot |  | 1 x $2
Balls |  | 2 x $0.25
Play Field Walls |  | 3 x $1
Total: |  | $189
BUDGET
Telecontroller Side | 
Physical specifications | 
Size (width x height x length) | 15 x 15 x 37 cm
Weight | 560 gr
Power Specifications | 
Idle Power | 8.03 W
Max Power | 8.03 W
Operation Time | 36 min
Operational Specifications | 
Screen Resolution | 800x480
Command Resolution | 8 bit
Robot Side | 
Physical specifications | 
Height | 27 cm
Diameter | 28 cm
Weight | 1710 gr
Power Specifications | 
Idle Power | 5.63 W
Max Power | 18.83 W
Operation Time | 38 min
Operational Specifications | 
Maximum Forward Speed | 0.45 m/sec
Maximum Rotational Speed | 2.3 rad/sec
TECHNICAL SPECIFICATIONS
Method of Solution
Command Interface : Joystick Command Transfer : 2.4 GHz RF Communication Video Transfer : FPV 5.8 GHz RF Communication Shooting : Push - Pull Solenoid Motion : Brushed DC Motor with Gear Box
Customer & Engineering Requirements
$200 budget 30+ meters indoor range Robot can hit, push or otherwise drive the ball but not grasp, scoop or otherwise carry it. Robot should transfer the ball to opponent’s half-field in less than 20 seconds.
Test Results
For video: For Command: Shoot Distance >1.5 m Up to 38 meters of overall playable distance
Test Results
Playable
Playable