## Slide 1
Potato Integrated Technologies
PITECH (Potato Integrated Technologies) was founded in 2018 with five shareholders from different backgrounds. As PITECH engineers our aim is to build a robot that we can control from a specified distance with a remote controller. This robot tries to score within a playfield in its opponent’s goal and defend its own goal.
Fatma Nur Arabacı - CEO
Furkan Bahadır ELİK - CTO
İrem COŞKUN - COO
Berkay GÖKSU - CMO
Aycan BEYENİR - CFO
SHAREHOLDERS
DELIVERABLES
Potato Robot Controller Unit 2 Li-Po Battery 6 Game Field Walls 2 Balls A Dummy Robot User Manual 2-year Warranty Software Pack
Special Thanks To our Supervisor Arzu Tuncay KOÇ
User friendly control module
Fast-learning curve for the user
Wide field of view
OUTSTANDING FEATURES
Materials |  | Cost
DC Motor with Gearbox |  | 2 x $15
L298N Motor Driver |  | 2 x $1.5
Push-Pull Solenoid |  | 1 x $4
Clone Arduino Uno |  | 1 x $4
Clone Arduino Mega |  | 1 x $10
FPV Drone Kit |  | 1 x $35
NRF24L01+PA+LNA SMA |  | 2 x $4
Joystick |  | 1 x $0.50
LCD screen |  | 1 x $30
900 mAh Li-Po Battery |  | 1 x $14
1350 mAh Li-Po Battery |  | 1 x $18
Buck Converter |  | 3 x $1
Plexiglass Chassis |  | 1 x $6
Standard Wheels |  | 2 x $2
Ball Wheel |  | 3 x $1
Cables & Connectors |  | $6
Structural connections |  | $3
Dummy Robot |  | 1 x $2
Balls |  | 2 x $0.25
Play Field Walls |  | 3 x $1
Total: |  | $189
BUDGET
Telecontroller Side | 
Physical specifications | 
Size (width x height x length) | 15 x 15 x 37 cm
Weight | 
Power Specifications | 
Idle Power | 8.03 W
Max Power | 8.03 W
Operation Time | 36 min
Operational Specifications | 
Screen Resolution | 800*480
Command Resolution | 8 bit
Robot Side | 
Physical specifications | 
Height | 27 cm
Diameter | 28 cm
Weight | 
Power Specifications | 
Idle Power | 5.63 W
Max Power | 18.83 W
Operation Time | 38 min
Operational Specifications | 
Maximum Forward Speed | 0.45 m/sec
Maximum Rotational Speed | 2.3 rad/sec
TECHNICAL SPECIFICATIONS
Method of Solution
Command Interface : Joystick Command Transfer : 2.4 GHz NRF Communication Video Transfer : 5.8 GHz FPV Communication Shooting : Push - Pull Solenoid Motion : Brushed DC Motor with Gear Box
Customer & Engineering Requirements
$200 budget 30+ meters indoor range
Test Results